## Slide 1: CSE-400 Fundamentals of Probability in Computing
Milestone - 1
Section -1
Group-13: Networks

## Slide 2: An Analysis of the Binary Exponential Backoff Algorithm in Distributed MAC Protocols
Application Domain: Wireless LANs (IEEE 802.11 DCF)
Distributed Medium Access Control (MAC) protocols
Real-World Context: Multiple wireless nodes compete for a shared channel Collisions reduce productivity and efficiency
Why Uncertainty is Intrinsic: Random backoff times
Random number of contending nodes Random collisions and idle slots

## Slide 3: Project Objective and Scope
Objective:
Develop an accurate analytical model for BEBA
Capture behaviors ignored by traditional models
What is being analyzed:
Channel state probabilities (Idle, Success, Collision)
Throughput performance
Impact of backoff randomness

## Slide 4: Project System Overview
End-to-End Pipeline: Stations generate random backoff
Channel contention occurs Channel state evolves over time
Major Components: Backoff mechanism
Channel state transitions Markov chain model
Throughput computation
Data Flow: Backoff choice → Slot access → Channel state → Performance metrics

## Slide 5: Sources of Uncertainty in the Project
Measurement Noise: Random slot outcomes
Variable collision duration
Environmental / Contextual Variability: Number of contending stations
Dynamic contention window sizes
Modeling / Data Uncertainty: Random backoff time distribution
Dependency between consecutive slots

## Slide 6: Key Random Variables and Their Roles
Primary Random Variables:
Backoff time r
Attempt probability τ Channel state Bk
What they represent:
r: Number of slots a station waits
τ: Probability a station attempts transmission Bk: Number of stations transmitting in a slot

## Slide 7: Probabilistic Reasoning and Inference
Uncertainty Propagation
Random backoff choices determine transmission attempts. Collisions double the backoff window, increasing randomness and affecting future
attempts.
Reasoning Support
Modeling backoff as a random variable allows estimating collision probability, successful transmission, and expected delay, inferring network behavior like throughput and stability.
Slot Transmission
Attempt transmission in selected slot
Backoff Update
Adjust window (double on collision)
Random Backoff
Select randomized delay
before attempt
Performance Metrics
Measure
collisions, delay, throughput
Channel Outcome
Idle, Success, or Collision occurs

## Slide 8: Operationalizing Probabilistic Reasoning
Simulation Implementation
Simulate N stations, each randomly selecting $r \in [0, 2^k - 1]$. Observe slot outcomes over thousands of trials using Monte Carlo simulation to estimate probabilities.
Simplifying Assumptions
Identical station behavior, continuous packet availability,
independent backoff choices, and ideal channel with perfect collision detection.
Metric
Probabilistic
Interpretation
Collision Rate | P(more than one station transmits in a slot)
Success Rate | P(exactly one station transmits)
Throughput | Expected successful transmissions per slot
Delay
Expected number of slots before success

## Slide 9: Current Limitations and Gaps
Known Weaknesses
Real Wi-Fi includes noise, hidden terminals, variable packet sizes, and hardware timing issues not modeled.
Unverified Assumptions
Backoff choices are assumed independent, and a constant number of active stations.
Conceptual Gaps
Real implementations may differ from theoretical BEB; physical
layer effects are ignored.

## Slide 10: Planned Refinements and Role Coordination
Next Milestone
Complete Python simulation of BEB.
Compare randomized BEB with deterministic waiting.
Generate graphs for collision probability, delay, and throughput.
Modeling Tasks
Validate simulation with theoretical expectations. Vary number of nodes and study behavior.
Analyze impact of contention window growth.
Role Coordination
Simulation Coding
Probabilistic Modeling
Graph Plotting & Analysis
Documentation & GitHub

## Slide 11: Summary of Group-Level Understanding
The Binary Exponential Backoff algorithm is a randomized protocol used in Ethernet and Wi-Fi networks to reduce repeated collisions. By modeling backoff as a random variable and simulating transmission attempts, we estimate collision probability, delay, and throughput. This project demonstrates how probability theory and randomized algorithms directly explain real network behavior and improve performance in shared communication channels.