## Slide 1: CSE-400 Fundamentals of Probability in Computing
Milestone - 3
Section -1
Group: s1_g13_net

## Slide 2: Project Context and Motivation
Binary Exponential Backoff Algorithm (BEBA)
Application: Wireless LAN (IEEE 802.11)
Problem: Multiple nodes share the same channel causing collisions
Uncertainty: Random backoff times, random node activity, random collisions
Goal: Use probability and simulation to analyze network performance

## Slide 3: Project Objective and Scope
Objective: Analyze BEBA using probabilistic modeling and simulation
Metrics studied:
  - Throughput
  - Collision probability
  - Channel state probabilities
Milestone-3 focus: Coding and simulation of the probabilistic model

## Slide 4: Project System Overview
System Pipeline:
1. Nodes generate packets
2. Nodes select random backoff
3. Backoff counter decreases each slot
4. Transmission attempt when counter = 0
5. Channel outcome: Idle / Success / Collision
Performance metrics measured from simulation

## Slide 5: Sources of Uncertainty in the Project
Measurement Noise: Random slot outcomes
Environmental Variability: Changing number of nodes
Modeling Uncertainty: Random backoff distribution
System randomness drives probabilistic behavior of the network

## Slide 6: Key Random Variables
r : Backoff counter value
τ : Transmission attempt probability
N : Number of stations
Bk : Number of transmitting stations
Channel state: Idle, Success, Collision

## Slide 7: Probabilistic Models and Assumptions
Backoff Distribution: Uniform(0, CW−1)
Assumptions:
- Saturated stations (always have packets)
- Ideal channel (no noise)
- All stations hear each other
- Time divided into discrete slots
- Independent transmission attempts across stations

## Slide 8: Probabilistic Reasoning
Random Backoff → Random Transmission Attempts
Number of transmitting stations follows Binomial distribution
Channel state probabilities:
P_idle = (1−τ)^N
P_success = Nτ(1−τ)^(N−1)
P_collision = 1 − P_idle − P_success

## Slide 9: Simulation Implementation
Simulation implemented using Python.
Simulation Method - Monte Carlo simulation over many time slots
Simulation Parameters
- Number of nodes: N = 10 - Number of slots simulated: 50,000 - Minimum contention window: CWmin = 4 - Maximum contention window: CWmax = 1024
Evaluation Metrics
- Throughput - Collision rate - Channel utilization

## Slide 10: Simulation Results
Observations
- Throughput increases initially with traffic - Higher traffic causes more collisions - Collisions reduce network throughput

## Slide 11: Current Limitations
Model Limitations
- Ideal channel assumption (no noise or interference) - Hidden terminal problem not modeled - Fixed number of nodes used in simulation
Simulation Limitations
- Simplified traffic generation model - Limited network size considered

## Slide 12: Planned Refinements and Role Coordination
Planned Refinements
- Compare simulation results with analytical probability model
- Study impact of increasing number of nodes on network performance - Analyze the effect of different contention window sizes
- Extend simulation to more realistic wireless scenarios
Role Coordination
- Simulation Coding: Implementation of BEBA simulation in Python
- Probabilistic Modeling: Mathematical analysis of backoff and transmission probabilities
- Graph Plotting & Analysis: Generating performance graphs and interpreting results
- Documentation & GitHub Management: Organizing code, reports, and project artifacts

## Slide 13: Summary
BEBA uses randomness to reduce collisions
Probability theory explains channel behavior
Simulation validates theoretical predictions
Randomized algorithms are essential for distributed network protocols